# Mathematical modeling of the impact of vehicles on water-saturated soil
## 1. Basic concepts of the physical and mechanical properties of soil
By their nature, soils are divided into two main classes: sands are products of mechanical destruction of basic rocks, and clays are products of chemical destruction of basic rocks. Sands and clays differ greatly in their physical and mechanical properties.
In nature, soils of mixed origin are usually found. They exhibit intermediate properties of sand and clay and are called, respectively, sandy loam, loam, etc.
All qualitative differences in soil properties are determined by the size and shape of the particles forming them. Of great importance in the manifestation of these properties is the water in the gaps between the particles. The gas in the soil (air, methane, water vapor) also strongly affects the properties of the soil.
Sands consist of particles having the shape of grains with a diameter of 0.5 - 2 mm (coarse sand) to 0.1 - 0.05 mm (fine sand) [47]. Clay particles are in the form of plates with a thickness of not more than 1 micron.

Let us introduce the notation.

v - some volume of soil

v_p - pore volume

v_s - volume of solid particles

v = v_p + v_s
%ivarphi = v_p over v - soil porosity

m = v_s over v - the volume of solid particles per unit volume of soil

%ivarphi + m = 1
%varepsilon = v_p over v_s = %ivarphi over m - coefficient of porosity.

Compressibility of soils
Due to the low permeability of solid soil particles, compression deformation occurs mainly due to a change in porosity. The relationship between the coefficient of porosity %varepsilon and compressive stresses %sigma is obtained using uniaxial compression devices. The curve is shown in Fig.1.1.

Fig.1.1: Compression curve

On small intervals of stresses change, it is approximated by a straight line

%varepsilon = - %alpha %sigma + %ALPHA	(1)

With a large number of loading and unloading, the soil becomes practically elastic.

Compaction factors %alpha , cm^{2}/kg (according to Florin)

Weakly compacted clays	0.10 - 0.01
Compacted clays	0.005 - 0.001

Porosity coefficients %varepsilon (according to Florin)

Sands	0.54 - 0.82
Compacted clays	0.67 - 1.2
Silt	1.00 - 3.00
Loams and clays	0.67 -1.00

Filtration properties of soils
The filtration rate is defined in soil mechanics as the flow rate of water through a unit of the geometrical area of ​​the soil section. Darcy's law establishes a relationship between the filtration rate q and the fluid pressure gradient H :
q=-k{partial H} over {partial s}
Where k is the filtration coefficient [cm / s]
H is determined in hydraulics by the formula:

H=P over %gamma + z , [cm]

Where P is the pressure in the liquid [ kG / cm^2 ]
 %gamma - specific gravity of the liquid [ kG / cm^3 ]
 z - the height of this point above the zero mark [cm].
The actual speed of water relative to immobile soil grains is determined by the formula:

u=q over %ivarphi

Where %ivarphi is the porosity of the soil (see above).
In the case of movement of soil grains towards the liquid at a speed v_r , Darcy's law is written in the form:

u - v_r = - {k over %ivarphi {partial H} over {partial s}} drarrow q - {%varepsilon}v = -k {partial H} over {partial s}	(2)

Filtration coefficient k , cm / s (according to Florin):
Sands 10^-2 - 10^-3
Clays 10^-6 - 10^-8

Understanding stresses in soil
Consider the case of deformation propagation in one plane. Let's select an elementary parallelepiped and call the ratio of the force acting on an elementary area to its area stress. Then, on the sections of the parallelepiped, inclined at different angles, we will get different values ​​of stresses. The stress vector coincides in direction with the force vector and it can be decomposed into normal and tangential components: %sigma_n and %tau (Fig. 1.2).

Fig.1.2
Let us introduce a rectangular coordinate system XoZ and denote the stresses acting along the oX and oZ axes, respectively, %sigma_x and %sigma_z .
Let only normal stress act in any section, and there is no tangential stress. This normal stress is called the main one. The largest and the smallest normal stresses acting in a given section are the main ones. They are denoted by %sigma_1 and %sigma_3 respectively.
It is convenient to determine the stress distribution in the sections of an elementary parallelepiped using Mohr's circles (Fig. 1.3).

Fig.1.3
It can be seen from the figure that in the section drawn at an angle %alpha , the values ​​of the normal and tangential stresses are determined by the coordinates of the point D on the circle. The maximum shear stress in absolute value is achieved at %alpha=+-%pi/4 .

The concept of soil strength
In soil mechanics, the main indicators of strength are considered to be the shear resistance of the soil. The maximum shear stress is determined from the equation:

%tau=c+%sigma_n{tan%varphi}	(3)

where c is called adhesion, and %varphi is the angle of internal friction. For sands c=0 , therefore %tau=%sigma_n{tan%varphi} , for clays, the cohesion and the angle of internal friction depend on the density of moisture. After preliminary compaction of the soil, an increase in adhesion and a decrease in the angle of internal friction are observed, this is associated with an irreversible decrease in the strength factor %varepsilon , as a result of which the molecular forces of interaction between particles increase [48].
From equation (3), you can determine the straight lines, which are called the lines of destruction. For a given value %sigma_1 , construct a Mohr circle so that it touches these lines (Fig. 1.4).

Fig.1.4
The slope of the fracture planes can now be determined. It makes an angle %pi/4+%varphi/2 to the line of action of the lowest principal stress. At this moment, the principal stresses satisfy the equation

%sigma_1=2c{sqrt{%lambda_%varphi}}+%sigma_3%lambda_%varphi	(4)

Where %lambda_%varphi=func tan^2(%pi/4+%varphi/2) , and the soil massif is in a state of so-called plastic limiting equilibrium [49]. The effect of the hydrostatic pressure of water in the pores of the soil should also be taken into account, therefore, the so-called effective stress, which is perceived by the skeleton of the soil, should be substituted in formulas (3) and (4), and their values ​​are less than the actual stresses by the value of the pore pressure of water. The sine of the largest deviation of the total stress vector can be represented as:
sin%theta_max=sqrt{(%sigma_x-%sigma_z)^2 + 4{%tau}xz^2} over {%sigma_z + %sigma_x + 2c/tan%varphi} .

Deformation modulus and Poisson's ratio
When compressing a soil sample in a compression device, transverse deformations of the soil are impossible. In this case, the lateral pressure coefficient %zeta is determined by the formula: %zeta=%sigma_x over %sigma_z . In soil mechanics, it is assumed that porosity depends only on the sum of the principal stresses, and not on their ratios. This assumption is based on the approximation of the real stress-strain curve by a straight line with sufficient accuracy for practical calculations. Because of this, we write formula (1) for the case of a biaxial stress state (plane problem):

%varepsilon=-a{%theta over {1+%zeta}} + A	(5)

Here %theta = %sigma_z + %sigma_z is the sum of the principal stresses.
The deformation modulus E(%varepsilon) is determined in soil mechanics from the expression:
de_x = 1 over {E(%varepsilon )} + (d%sigma_x - %nu d%sigma_z) ,
where %sigma_х and %sigma_z is the increment in stresses, that caused de_x - the strain increment along the oX axis.
Poisson's ratio %nu is defined through the lateral pressure ratio %zeta : %nu = %zeta over {1 + %zeta} .
If we take the dependence %varepsilon = %varepsilon(%theta) as linear, for example, in the form (5), we obtain
E = {%beta (1 + %varepsilon) } over %alpha ,
Where %beta = {(1-%zeta )(1+2%zeta)} over (1 + %zeta) .

Lateral pressure coefficient (according to Florin):
Sands 0.40-0.42
Clays 0.70-0.75.
The above expressions for the deformation moduli make it possible, in the case of a nonlinear relationship between stresses and strains, to determine the modulus value for any given stress state. However, in many cases it is more convenient to use the so-called average deformation modulus E_avg = {%beta (1 + %varepsilon_1) } over %alpha , where %varepsilon_1 is the initial porosity coefficient.
It was shown (N.M. Gersevanov) the constancy of E_avg for plastic soils in a small range of load variation.
In conclusion, let us consider the case of applying a vertical load along the rectilinear boundary of a linearly deformed medium. In this case [51]:

%sigma_x = 1 over 2 %theta + 1 over 2 z {partial%theta} over {partial{z}} / %sigma_x = 1 over 2 %theta + 1 over 2 z {partial%theta} over {partial{z}} / %tau_xz = - {1 over 2 z {partial%theta} over {partial{x}}}	(6)

The stress components are determined by the formulas:

%sigma_x = %lambda e + %nu %varepsilon_x
%sigma_z = %lambda e + %nu %varepsilon_z ,
where %varepsilon_x = {partial u_1} over {partial x} , %varepsilon_z = {partial u_3} over {partial z} , %lambda = {%nu E} over {(1 + %nu) (1 - 2 %nu)} , e = %varepsilon_x + %varepsilon_z ,
u_1 и u_3 - displacement components.
%tau_xz = %nu %gamma_xz ,
where %gamma_xz = {partial u_1} over {partial z} + {partial u_3} over {partial z} .
For a general model of a linearly deformable medium, the stresses in the soil skeleton must satisfy the equations [51]:

{partial %sigma_x} over {partial x} + {partial %tau_xz} over {partial z} + X = 0	(7)

{partial %sigma_z} over {partial z} + {partial %tau_xz} over {partial x} + Z = 0	(8)

Where X и Z - components of volumetric forces,
and the equation

%DELTA(%sigma_x + %sigma_z) = - {1 over {1 - %nu}}({partial X} over {partial x} + {partial Z} over {partial z})	(9)

Where %nu - коэффициент Пуассона , %DELTA - оператор Лапласа.
## 2. Mathematical formulation of the compaction problem
### 2.1. The Simplest One-Dimensional Compaction Problem
Key assumptions:
a) We consider models of a two-component soil consisting of solid particles and water filling its pores. This model is called soil mass. “The question may arise: in what cases, in practice, are we dealing with a soil mass? ... As for the ground lying above the groundwater level, in the vast majority of cases it is a soil mass, that is, one in which all voids are filled with water due to the capillary rise of water in the fine pores of the soil. In clays, the length of the capillary rise of water can reach a height of over 300 m above the groundwater level.
In order to judge whether we have a soil mass above the groundwater level, we can be guided by the following signs: in all cases when the soil is in a fluid, plastic and semi-solid state, we are dealing with a soil mass. Only when the soil passes from a semi-solid state to a solid state does air penetrate into the pores of the soil and partially fill the voids of the soil skeleton. The transition from solid to solid is characterized by a sharp change in the color of the soil. … To determine the condition of the soil, i.e. whether it is fluid, plastic or semi-solid, there are fully developed laboratory methods ... ”(NM Gersevanov, [50, p. 145]).
b) the change in porosity occurs only due to the dense packing of soil particles;
c) the filtration coefficient does not depend on the stress state.
Basic equations.

{partial u_z} over {partial z} + {partial n} over {partial t} = 0	1

{partial v_z} over {partial z} + {partial m} over {partial t} = 0	2

Here, as before, v_z u_z and are the flow rates of the solid and liquid components along the oZ axis. Adding equations (1), (2) and taking into account equality n+m=1 , we obtain

{partial u_z} over {partial z} + {partial v_z} over {partial z} = 0	3

2. Darcy's dependency.

u_z - %varepsilon v_z = -k {partial H} over {partial z}	4

3. Equilibrium equation.
Let %sigma - stress in the soil skeleton; p - pressure in water; %sigma^{"*"} and p^{"*"} - the corresponding values ​​in a state of complete stabilization.
%sigma + p = %sigma^"*" + p^"*"	5

That is the sum of stress and pressure is a constant.
Differentiate (4) by z :
{partial u_z} over {partial z} - {partial %varepsilon} over {partial z} v_z - %varepsilon {partial v_z} over {partial z} = - {partial over {partial z} {(k {partial H} over {partial z})} }

considering (3):
v_z {partial %varepsilon} over {partial z} + (1 + %varepsilon){partial v_z} over {partial z} = {partial over {partial z} {(k {partial H} over {partial z})} }
Further, taking into account (2) and the relationship between %varepsilon and m from Section 1, we obtain:
{partial v_z} over {partial z} = - {{partial m} over {partial t}} = - { partial over {partial t} (1 over {1 + %varepsilon}) } = 1 over (1 + %varepsilon)^2 {partial %varepsilon} over {partial t}

v_z {partial %varepsilon} over {partial z} + (1 + %varepsilon){partial v_z} over {partial z} = {partial over {partial z} {(k {partial H} over {partial z})} }
Further, as shown in [52],
v_z {partial %varepsilon} over {partial z} = o({partial %varepsilon} over {partial t})
and the error from replacement [1 + %varepsilon(t,z)] by [1 + %varepsilon(t,z)] ( %varepsilon is the average porosity in the considered compaction range) is less than the error of the laboratory determination of the filtration coefficient k .
In view of the above
{partial %varepsilon} over {partial z} = (1 + %varepsilon) {partial over {partial z} {(k {partial H} over {partial z})} }

{partial %varepsilon} over {partial t} = {d %varepsilon} over {d %sigma} {partial %sigma} over {partial t} = - a (- {{partial p} over {partial t}}) = a %gamma {partial H} over {partial t} .

Here we used equation (1) from Section 1 and equilibrium equation (5). We will finally write down

{partial H} over {partial t} = {(1 + %varepsilon) over {a %gamma}}{partial over {partial z} {(k {partial H} over {partial z})} }	6

The resulting equation is equivalent in form to the equation of heat conduction and diffusion.
Next, the initial and boundary conditions are assigned:
t = 0, " " H = H(Z)

t > 0, " "z = 0: " " H = %lambda(t), " " z = z ^"*": " " H = %mu(t) .

Example. Let the distributed load be instantaneously applied at the initial moment t = 0 . If the layers z = 0 and z = z^"*" are also permeable, then when t > 0 :
z = 0, " " H = 0; " " z = z ^"*", " " H = 0 ,
For waterproof layers {partial H} over {partial z} = 0 .
The solution of equation (6) together with the given initial and boundary conditions is found by known methods, for example, by the method of separation of variables (by the Fourier method). The stress distribution %sigma(z,t) is determined from equation (5):
%sigma + p = Const = q

%sigma = q - p = q - %gamma H .

The amount of compaction can be found by the formula:
s(t,h) = int_o^h e_z(t,z)dz
where e_z is the compaction of the layer with the coordinate z , according to the results of Section 1
e_z = a over {1 + %varepsilon} %sigma ;
h - active compaction depth, can be determined in the following way:
make up a sequence (h_k), k = 0,1,2... and determine (h_k), k = 0,1,2... from the condition:
abs{s(t,h_{l-1}) - s(t,h_l)} over {s(t, h_l)} <= %delta
Where %delta is the specified accuracy. Thus, the problem of compaction in the one-dimensional case can be considered solved.
### 2.2. Plane and spatial problems of compaction
The assumptions are the same as in the previous paragraph. First, consider the planar compaction problem (XoZ plane).
Basic equations.
1. Equations of continuity

{partial u_x} over {partial x} + {partial u_z} over {partial z} + {partial n} over {partial t} = 0	1

{partial v_x} over {partial x} + {partial v_z} over {partial z} + {partial m} over {partial t} = 0	2

add equations (1), (2)

{partial (u_x + v_x)} over {partial x} + {partial (u_z + v_z)} over {partial z} = 0	3

2. Darcy's dependence.

u_x - %varepsilon v_x = - k {partial H} over {partial x}	4

u_z - %varepsilon v_z = - k {partial H} over {partial z}	5

3. Equilibrium equations.

%sigma_x + p = %sigma_x^"*" + p^"*"	6

%sigma_z + p = %sigma_z^"*" + p^"*"	7

%tau_xz = %tau_xz^"*"	8

Here %tau are the shear stresses. It is assumed that the tangential load is instantly perceived by the skeleton and is not transmitted to the water.
Differentiate (4) by x , (5) by z and add

{partial u_x} over {partial x} + {partial u_z} over {partial z} - %varepsilon ({partial v_x} over {partial x} + {partial v_z} over {partial z}) = - [partial over {partial x} (k {partial H} over {partial x}) + partial over {partial z} (k {partial H} over {partial z})] .

Comment. Discarded terms {partial %varepsilon} over {partial z} v_z and {partial %varepsilon} over {partial x} v_x .

Taking into account (3), we obtain

(1 + %varepsilon) ({partial v_x} over {partial x} + {partial v_z} over {partial z}) = {partial over {partial x} {(k {partial H} over {partial x})} } + {partial over {partial z} {(k {partial H} over {partial z})} } ,

where the value 1 + %varepsilon is a constant (see section 2.1).
Further, from (2) we have
{partial v_x} over {partial x} + {partial v_z} over {partial z} = - { {partial m} over {partial t}} = 1 over (1 + %varepsilon)^2 {partial %varepsilon} over {partial t} ,
taking this into account, we get

{partial %varepsilon} over {partial t} = (1 + %varepsilon) [ {partial over {partial x} {(k {partial H} over {partial x})} } + {partial over {partial z} {(k {partial H} over {partial z})} }]	9

Next, we use equation (6) from Section 2.1. We have

{partial %varepsilon} over {partial t} = {d %varepsilon} over {d %sigma} {partial %sigma} over {partial t} = - {a over {1 + %varepsilon} } {partial %theta} over {partial t} .

From equation 6-7 we get
%theta = %sigma_x + %sigma_z = %theta^"*" = %sigma_x^"*" + %sigma_z^"*" - 2 (p - p^"*")
so
{partial %theta} over {partial t} = - 2 {partial p} over {partial p} = -2 %gamma {partial H} over {partial t}

Let us finally write equation (9) in the form:

{partial H} over {partial t} = {(1 + %varepsilon) (1 + %varepsilon) } over {2 %gamma a} [ {partial over {partial x} {(k {partial H} over {partial x})} } + {partial over {partial z} {(k {partial H} over {partial z})} }]	10

Reasoning quite similarly in the case of a triaxial stress state, we arrive at the equation:

{partial H} over {partial t} = {(1 + %varepsilon) (1 + 2%varepsilon) } over {3 %gamma a} [ {partial over {partial x} {(k {partial H} over {partial x})} } + {partial over {partial y} {(k {partial H} over {partial y})} }+ {partial over {partial z} {(k {partial H} over {partial z})} }]	11

Let us assume that the filtration coefficient k does not change during the compaction process. Then we have:
{partial H} over {partial t} = K %DELTA H	12

Where %DELTA is the Laplace operator,

K = {(1 + %varepsilon) (1 + %varepsilon) } over {2 %gamma a}k - for a plane problem

K = {(1 + %varepsilon) (1 + 2%varepsilon) } over {3 %gamma a}k - for a spatial problem.
Initial conditions
Note that the initial pressure distribution function H_0 satisfies the Laplace equation

%DELTA H_0 = 0	13

This equation is a consequence of the fact that at the initial moment of load application

{partial v_x} over {partial x} = {partial v_y} over {partial y} = {partial v_z} over {partial z} = 0

We find the initial pressure distribution from (6) and (7):
in the case of the plane problem
P_o = 1 over 2 %theta_0^"*" + P_0^"*" ,	14

for a spatial task

P_o = 1 over 3 %theta_0^"*" + P_0^"*" .	15

Here, as before, %theta_0^"*" denotes the sum of normal stresses in a stabilized state, P_0^"*" -is the final pressure distribution. We accept further P_0^"*" = 0 .
Thus, to determine the initial distribution of the pressure, it is necessary to solve problems (7), (8) and (9) of the theory of elasticity (Section 1).
The initial stress distribution is determined from (6), (7), (14), (15)
For a flat problem
%sigma_x0 = 1 over 2 (%sigma_x^"*" - %sigma_z^"*")
%sigma_z0 = 1 over 2 (%sigma_z^"*" - %sigma_x^"*")
%tau_xz0 = %tau_xz^"*" .
For a spatial task
%sigma_x0 = %sigma_x^"*" - 1 over 3 %theta^"*"
%sigma_y0 = %sigma_y^"*" - 1 over 3 %theta^"*"
%sigma_z0 = %sigma_z^"*" - 1 over 3 %theta^"*"
%tau_xz0 = %tau_xz^"*", " "%tau_xy0 = %tau_xy^"*", " "%tau_yz0 = %tau_yz^"*" .

Border conditions
On the permeable sections of the boundary surface, the values ​​of the pressure function are equal to zero : H = 0, x in %GAMMA . In watertight areas, the pressure gradient value is zero:
{partial H} over {partial n} = 0, x in %GAMMA .
In addition, in the case of compaction of heterogeneous soil, the conjugation conditions must be met at the border of adjacent media:
H_1(x,t)"|"_S = H_2(x,t)"|"_S
k_1({partial H_1} over {partial n}) = k_2({partial H_2} over {partial n}) .

Example. The plane problem of compaction of isotropic soil with an arbitrary vertical load. We find the initial stress distribution from equation (6) in Section 1 and from equations (6), (7), (8):

%sigma_x0 = 1 over 2 (%sigma_x^"*" - %sigma_z^"*") = 1 over 2 z {partial %theta^"*"} over {partial z} = z {partial P_0} over {partial z} newline %sigma_z0 = 1 over 2 (%sigma_z^"*" - %sigma_x^"*") = -z {partial P_0} over {partial z} newline %tau_xz0 = %tau_xz^"*" = 1 over 2 z {partial %theta^"*"} over {partial x} = -z {partial P_0} over {partial z} .	16

To determin P_0 , it is necessary to solve the following problem:
%DELTA P_0 = 0 ,
z = 0, x in D " " P_0 = q(x) newline - given load,
x notin D " " P_0 = 0; newline x toward +-infinity, " " z toward +-infinity, " " P_0 = 0	17

Consider a more general first boundary value problem:
Lu = -f(M), " " (M in D) newline u"|"_S = %varphi(M)	18

In the original problem
u equiv H, " " Lu = %DELTA u = {partial^2 u} over {partial x^2} + {partial^2 u} over {partial z^2} ;
f(M) = f(x,z) = 0, (M in D) ;
%varphi(M) = %varphi(x,z) ""equiv"" left lbrace stack {0, "" z = 0, "" x notin [-a, a] # q(x), z = 0, "" x in [-a, a] # 0, "" z toward +infinity, "" x toward +- infinity} right none
where q(x) = %gamma %rho (x) is the diagram of the load distribution, 2a is the contact width (Figure 2.1).
To solve problem (18), the method of Green's functions is used, the solution has the form [53]:
Fig.2.1
u(P) = - int_S%varphi {partial G} over {partial n} dS_M
where G = G(M,P) is the solution to an equation of a special form:

left lbrace stack {%DELTA G = - %delta(M,P) " "(M in D) # G"|"_S = 0 } right none	19

Here %delta(M,P) - %delta is the Dirac function. Solution (19) is presented in the form:
G(M,P) = %psi (%GAMMA_MP) + V(M,P) ,
where V - is harmonious at D (i.e. %DELTA V = 0, "" M in D ), and %psi(%GAMMA_MP) has a singularity at the point P and at %GAMMA_MP = 0

%DELTA %psi = - %delta(M,P)	20

We integrate (20)
int_{S_P^R} %DELTA %psi ds = -1 ( %delta function property)
Using Green's formula, we pass to the integral over a circle centered at the point P of radius R (see Figure 2.1):
stack {lint_C { {partial %psi} over {partial n}}ds = lint_C { {d %psi} over {dr}}ds = {d %psi} over {dr}"|"_R cdot {2 %pi R} = -1# d%psi(R) = - {1 over {2 %pi} dR over R} toward %psi(R) = - {1 over {2 %pi} }ln 1 over R# toward G(M,P) = {1 over {2 %pi} }ln (1 over %GAMMA_MP) + V(M,P) }
For our case V(M,P) is determined by the method of reflections (Figure 2.2).
Due to the fact that on the boundary of the half-plane G(M,P) = 0 , it follows that V(M,P) = - {1 over {2 %pi} ln(1 over %GAMMA_{MP_1}) } is a harmonic function forall M in D
Fig.2.2
toward G(M,P) = 1 over {2 %pi} ln(1 over %GAMMA_MP) - {1 over {2 %pi} ln(1 over %GAMMA_{MP_1}) }
иor in coordinates x, z, %xi, %eta : ""(M(%xi, %eta), P(x,z)) :
G(M,P) = 1 over {2 %pi} ln(1 over sqrt{(x-%xi)^2 + (z - %eta)^2}) - { 1 over {2 %pi} ln(1 over sqrt{(x-%xi)^2 + (z + %eta)^2})}
drarrow "" u(P) = - int_a^-a %rho(%xi) {partial G} over {partial %eta}"|"_{%eta=0}d %eta , and it remains to find
{partial G} over {partial %eta}"|"_{%eta=0} = 1 over {2 %pi} ln(2z over {(x-%xi)^2 + z^2 })
So solution (18):
u(P) = 1 over %pi int_a^-a %rho(%xi) z over {(x-%xi)^2 + z^2 }d%xi
for the original problem, this is equivalent to the following expression:
H_0(x,z) = 1 over %pi int_a^-a %rho(%xi) z over {(x-%xi)^2 + z^2 }d%xi
So found in the initial pressure distribution:
P_0(x,z) = %gamma over %pi int_a^-a %rho(%xi) z over {(x-%xi)^2 + z^2 }d%xi
where %rho(%xi) = {q(%xi)} over %gamma , that is, you can rewrite

P_0(x,z) = 1 over %pi int_a^-a q(%xi) z over {(x-%xi)^2 + z^2 }d%xi	21

We find the initial stress distribution by the formulas (16):

%sigma_x0 = z {partial P_0} over {partial z} = z over %pi int _{-a} ^a q(%xi){(x - %xi)^2 - z^2} over {[(x - %xi)^2 + z^2]^2} d %xi newline newline %sigma_z0 = - %sigma_x0 newline newline %tau_xz0 = -z {partial P_0} over {partial z} = 1 over %pi int _{-a} ^a q(%xi){2z(x-z)} over {[(x - %xi)^2 + z^2]^2} d %xi	23

The distribution of initial stresses and pressures for an arbitrary vertical load is shown in Figures 2.3 and 2.4.

Fig.2.3 The distribution of initial stresses in a homogeneous environment	Fig.2.4 The distribution of initial pressures in a homogeneous environment